QUEENSLAND BLIND ASSOCIATION INC.

T43

ORICOM AMPLIFIED BIG BUTTON PHONE

WARNING

Before installing or removing batteries, make sure the telephone is NOT connected to the telephone socket.

CONNECTING THE TELEPHONE

- Connect the handset curly cord.

- Locate the battery compartment on the base of the phone.  Using a small Phillips head screwdriver unscrew the small screw and slide back the battery compartment door in the direction of the arrow.

- Insert 4 AAA 1.5V alkaline batteries (supplied) in the    battery compartment, observing the correct polarity.

Butteries must be installed of you wish to increase the ring level by 10 dB.

- Replace the battery door and replace the retaining screw.

- Connect the telephone line cord.

- Connect the telephone plug to the wall socket

RINGER SETTINGS

A switch located on the side of the telephone allows the ringer to be switched Hi, Low and Off by sliding from left to right.

Your phone comes with the ringer switched to High and the melody set to 6.

Melody 1	1 (low)	2 (mid)	3 (high)

Melody 2	4 (low)	5 (mid)	6 (by default)

Melody 3	7 (low)	8 (mid)	9 (high)

If you don’t like the ringer melody, you can choose a new one by changing the settings as follows:

- Lift the handset

- At the bottom of the keypad is a set of four small buttons. Press the third button.

- Press the hash button

- Press any button 1 to 9

Ringer will be activated on next call.

RECALL SWITCH

You will use the RECALL button (R) (the second button at the bottom of the device) when using your network operator’s services such as call waiting etc. If this feature is not working check the position of the Recall switch (second button) on the base of the phone.  It should be set at 100ms.

WALL MOUNTING

To wall-mount your telephone, slide out the clip (located in the base unit, just below the ear piece), turn around and slide back into the wall mounting position. This will ensure that the handset stays firmly in position.  Drill 2 holes in the wall 80mm apart, insert the wall plugs into the wall if required.  Insert two screws (not supplied).  The screws should protrude from the wall 6-7mm.  Place the phone onto the screw-heads and slide down to secure.

If you are using this telephone with a hearing aid, set you hearing aid to the “T” setting.

ANSWERING AN INCOMING CALL

- When and incoming call is received the phone will ring and flash, to answer the call lift the handset and speak.

- On completion of the call, carefully replace the handset in the cradle to release the line.

VOLUME AND TONE RECEIVING ADJUSTMENT

You can increase the volume and adjust the receiving tone according to your own hearing requirements.

The small oval button at the top right hand corner allows extra receiving and tone functions to be activated during the conversation.  When the function is activated, the red light located near the button is lit.

Adjust the tone and volume levels with the slide switches located to the left according to your own hearing requirements.

MAKING A CALL

- Lift handset and dial required number

- On completion of the call, replace the handset in the cradle.

SENDING VOLUME ADJUSTMENT

If your voice is quiet or called parties have difficulty hearing you, you can increase the sending level volume with the small switch located on the right side.  You can also decrease the sending volume if required.

LAST NUMBER REDIAL

- Lift the handset

- Listen for dial tone and press the first small oval button at the bottom left hand corner of the device.

Note:  The previously dialled number will be automatically redialled (not in use for memory numbers).

MUTE BUTTON

If you wish to speak privately to someone else, hold the fourth small oval button at the bottom of the device. You will still be able to hear the callers but they cannot hear you during the mute operation.  To resume normal conversation, release the button.

STORING TELEPHONE NUMBERS

Your phone can store 12 one touch memories (21 digits maximum for each memory)

To store a number please follow instructions below:

- Lift the handset

- Press the third small oval button at the bottom of the device

- Press M1, M2, ….., or M9 or P1, P2, P3 numbers to store your number (these are larger oval buttons located at the very top of the telephone and along the right hand side of the telephone)

- Dial the number you wish to store

- Press third small oval button at the bottom of the device button again

Note:  Numbers will be lost after a few hours if you disconnect your phone.  Entering a new number in memory will automatically erase the previous number stored in that location.

DIALLING STORED NUMBERS

- Lift the handset and await the dial tone.

- Press appropriate button M1, M2, ….,or M9 or P1, P2, P3, (these are larger oval buttons located at the very top of the telephone and along the right hand side of the telephone)

- The stored number will be dialled automatically.  For easy reference to the numbers you have stored in memories M1-M9, use the index card located under the base of the phone.