QUEENSLAND BLIND ASSOCIATION INC.

P104

TEL-TEMP INDOOR/OUTDOOR

TALKING THERMOMETER

Features:

Voice Announcement – Announces both indoor and outdoor temperatures in true human voice.

Announcement at Alarm – Lets you hear the temperature announcement at the preset alarm time.

Hourly Temperature Announcement – Lets you hear the temperature every hour except between 9pm and 7am, so as not to disturb your sleep.

High Temperature and Freezing Point Alerts – Alerts you when the temperature goes above 38°C (100°F) or below 0°C (32°F).

Daily High/Low Temperatures – Lets you find out daily highest and lowest temperatures.

Period Max/Min Temperatures – Lets you find out the maximum and minimum temperature in a specific time frame.

Volume Control and On/Off – Lets you adjust or turn off the volume of the announcements.

°C and °F – Lets you choose your temperature scale.

Installing the Batteries

Your thermometer is powered by two AAA batteries. We recommend alkaline batteries.

The battery compartment is located on the back of the thermometer at the top.

- Slide off the battery compartment door in the direction of the arrow.

- Remove the old batteries and place two fresh AAA batteries in the compartment at the correct polarity. The thermometer sounds four beeps and displays both the indoor and outdoor temperatures.

- Replace the battery compartment door.

It is recommended that the batteries be removed from the thermometer if you not use the unit for a long period of time.

Mounting the Thermometer and Remote Probe

Your thermometer is designed for both wall mount and desk-top use. The indoor temperature probe is located inside the thermometer unit. The outdoor temperature probe (remote probe) is connected to the unit by a cable and should be placed outside the house.

- Select the location where the thermometer will be used. If wall-mounted, first drive a screw into the wall, then hang the thermometer using the hole on the back of the unit.

- Route and secure the outdoor probe cable from the thermometer unit through the window to outside the house.

- Secure the probe to the outside wall using a screw.

Caution:

- Do not place the thermometer or its remote probe where they will be in direct sunlight which may cause erroneous reading.

- Keep the thermometer and remote probe away from hot or cold sources such as stoves, heating and air conditioning vents and radiators.

- Do not place the thermometer in water or in a location where it is likely to get wet.

Adjusting the Volume

Slide open the lower cover to expose function control buttons. Press the Volume button on the far left of the top row to select the volume of announcements and the chime.

The display indicates three choices: <<<<( for high volume, <<( for low volume, and no display for volume off.

Changing the Mode

Pressing the Mode button, on the far left of the bottom row, will cycle the unit through four LCD display modes.

- One beep displays the indoor temperature at the top of the screen and the time at the bottom of the screen.

- Two beeps displays the time at the top of the screen and the outdoor temperature at the bottom of the screen.

- Three beeps displays the time at the top of the screen and the alarm time at the bottom of the screen.

- Four beeps displays indoor temperature at the top of the screen and outdoor temperature at the bottom of the screen.

Setting the Time

- Press Mode until one beep is heard and the time shown on the lower display.

- Repeatedly press Hr Set, the middle button on the top row, to set the current hour.

- Repeatedly press Min Set, to the right of the Hr Set button, to set the current minute.

Announcing the Current In/Out Temperature

To announce the current indoor/outdoor temperature, press the Talking button above the control panel. The unit will always announce the In/Out temperature regardless of which of the four display modes you are in.

Turning the Hourly Announcement On or Off

You can set the thermometer to announce the current indoor/outdoor temperatures at the beginning of each hour.

To turn on the hourly announcement, slide Hr Report left to the ON position, (((())) appears on the display. This switch is on the second button on the top row. There will be no announcement between 9pm and 7am.

To turn off the hourly report, slide Hr Report switch right to the OFF position.

Using the Alarm for Temperature Announcement

You can have the thermometer report the In/Out temperature at a preset alarm time.

- Press Mode repeatedly until the unit sounds three beeps and the alarm time shows in the lower display. The alarm time has “AL” in between the hour digits and the minute digits.

- Repeatedly press Hr Set to set the alarm hour. The display shows PM for a PM hour.

- Repeatedly press Min Set to set the alarm minute.

- Press the ALM ON/OFF button in the middle of the bottom row to turn the alarm on. A picture of a bell will appear on the display.

- Make sure the volume is on. There will be no announcement if the volume is set to 0.

At the preset alarm time, the unit announces the In/Out temperature five times. Then the unit announces once in every 15 minutes for the first hour. To silence the alarm during its announcement, press Talking. To turn the announcement off completely, press Alm On/Off.

Announcing Daily High/Low Temperature

This unit records daily lowest and highest temperatures and the time at which these temperatures occur.

- Press Daily Min/Max, on the far right of the top row, to announce the indoor highest temperature. The upper display shows the temperature and the lower display indicates the time at which the highest temperature occurs. DAILY MAX appears on both displays.

- Press Daily Min/Max again to announce the indoor lowest temperature.

- Press Daily Min/Max again to announce the outdoor highest temperature.

- Press Daily Min/Max again to announce the outdoor lowest temperature.

- To return to normal display mode, press the Daily Min/Max button again, or press no button for 1 minute.

Announcing Manual Min/Max Temperature

This unit can record the maximum and minimum temperatures during a specific time period.

- Press Clear, the fourth button on the bottom row, to reset the memory. The unit will start to record the minimum and maximum temperatures from then on.

- Press Manual Min/Max, the far right button on the bottom row, to announce the indoor lowest and highest temperatures between the time when the memory was cleared and the time when you press the button.

- Press Manual Min/Max again to announce the outdoor lowest and highest temperatures.

- To return to normal display mode, press the Manual Min/Max button again, or press no button for 1 minute.

High Temperature and Freezing Point Alerts

When the indoor or outdoor temperature is above 38°C (100°F) or below 0°C (32°F), the unit will alert you by reporting the current outdoor and indoor temperatures three times. A flashing sun appears on the display for temperatures above 38°C (100°F), or a flashing snowflake for temperatures below 0°C (32°F). These symbols will continue to show on the display until the temperature is back to normal.

Selecting °C or °F

The announcement and display can be set to either °C or °F. Slide the [°C or °F] switch to the left for °C, or to the right for °F.