QUEENSLAND BLIND ASSOCIATION INC.

L010

BRAILLE LABELLER

Tape Specification: To be used with 9mm or 12mm wide tape.

Loading/Reloading Vinyl Labelling Tape

- Lift handle cover located at the top of the handle.

- Before placing tape roll into tape compartment, pull several inches of tape out and feed it by hand into Braille labelling guide.

- Place vinyl labelling tape into tape compartment located in handle.

- Close handle cover. Labeller is ready to print.

Imprinting Braille Characters

- Rotate the circular Braille disc to select the Braille letter or number until it sits in the opening of the labelling guide. Use letters and numbers imprinted on the lower disc to identify corresponding Braille signs.

- Firmly squeeze and then release the trigger on the handle to make impression of the selected character. In order to create a blank space or to advance the tape, lightly squeeze on the trigger until you hear an audible click, then release the trigger.

Cutting Vinyl Labelling Tape

- Rotate the circular Braille disc until the rectangle shape sits in the opening of the labelling guide.

- Firmly squeeze and then release the trigger on the handle to cut Labelling tape.

- Advance labelling tape (lightly squeeze the trigger until you hear and audible click, then release the trigger) several spaces to remove cut tape.

Removing Circular Braille Disc

- Remove labelling tape from labeller by opening handle cover at the top of the handle.

- Firmly hold circular Braille disc on both sides and pull circular Braille disc approximately 6mm away from the handle.

- Lift up circular Braille disc and remove.

Installing Circular Braille Disc

- Align small tab located at the bottom of the circular Braille disc with labelling guide and gently push the disk toward the handle until it snaps back into position.

- Load vinyl labelling tape into labeller by opening handle cover at the top of the handle.