QUEENSLAND BLIND ASSOCIATION INC.

K114

## LIQUID LEVEL SENSOR – SAY WHEN

The liquid level sensor (Say When) is an aid for people with vision impairment to fill cups and glasses with liquid without overfilling.

Using the sensor

- Simply hang the sensor over the cup or glass with the metal probes on the inside of the container.

- Slowly pour in your liquid until a continuous tone is heard.

### Care and Maintenance

Simply wipe the probes with a dry cloth after use.

Do not immerse the liquid level sensor in liquid.  If the unit fails to operate or a continuous tone is heard after accidental immersion, then remove the battery and allow to dry with the back cover removed.

### Battery Life and Replacement

The liquid level sensor only consumes battery power when in use and there the batteries should last for at least 12 months with normal use.  Replace if sound becomes weak.

Removing the battery – Hold the units ORANGE body at about its mid-point and pull the battery out with your other hand (a slight side to side motion may help)

Fitting the new battery - The standard 9-volt battery used has 2 terminals which are different shapes, which mate with corresponding contacts inside the ORANGE sensor body.

1.	Plug the battery into the ORNAGE sensor body.

2.	Place your thumb at the bottom of the battery and your index finger on the top of the ORANGE sensor body.

3.	Squeeze your fingers together until you feel the battery click into position.

**  If the unit produces a buzzing sound whilst fitting a battery, then the unit has given a wrong battery insertion warning.  Pull the battery out and turn battery around and try again.