QUEENSLAND BLIND ASSOCIATION INC.

K007

TALKING KITCHEN SCALES

Please Note: The manufacturer specifies if this item is faulty and you want to return it, you must return it with the original Warranty Card and receipt as proof of purchase, otherwise we cannot tell the actual purchase date of if you were the original purchaser and we must assume it’s out of warranty. Without this card, we cannot facilitate a repair or refund with the manufacturer. Please keep the Warranty Card in a safe place.

Battery Installation

- Press and push open the battery cover located on the back of the unit.

- Insert one 9V size battery with correct polarity.

- Close the battery cover until it clicks shut.

Weighing Function

- There are four (4) buttons on the scale. Turn the scale on by pressing the “ON” button (fourth button). It will say “Hello”. Once the platform is stable, it will say “I’m ready” and display “0g”.

- Place the item to be weighed onto the scale platform. The weight will be displayed and read out once the reading is steady.

- There is a stability indicator “H” in the top left corner of the screen. Whenever the weight is stable, the “H” will be displayed before the voice reading.

- Turn the scale off by pressing the “OFF” button (third button). It will say “Good-bye”.

NOTE: The scale will beep twice and show “ERR” if it is trying to weight above its capacity.

The voice reading function only responds to changes of more than 5g.

To Select oz or gram

Use the “G/OZ” button (second button) to select the desired unit.

To Use TARE Function

Turn on the scale using the fourth button. Place the empty container on the weighing platform. Press the “TARE” button (first button). Place the items to be weighed into the container. The exact weight of the items will show.

To Add the Weight Value

Press “TARE” (first button) to zero the value of the items being weighed. Without removing the items, add the next item. The scale will show the weight of the added item.

The process can be repeated as many times as necessary.

NOTE: The scale will beep three times to represent negative readings when using TARE function.

Auto Power Down

The scale turns off automatically if left idle for about 60 seconds.

Switching the Talking Function On/Off

Use the switch at the back bottom corner of the scale to switch the speaker function on or off by sliding the button left and right.

Precautions

- Do not clean the unit with abrasive or corrosive compounds. It may scratch the plastic and corrode the electronic circuit.

- Do not overload the scale. Placing items weighing over 3000g may cause permanent damage to the scale and void your warranty.

- Do not subject the unit to excessive force, shock, dust, temperature, direct sunlight, heavy rain or humidity, as this may result in malfunction, shorter electronic life span, battery damage or distorted parts.

- Do not tamper with the unit’s internal components. It will invalidate the warranty on the unit and may cause unnecessary battery damage and distorted parts.

- Place product on flat surface before use.